## Slide 1: Communication protocols

## Slide 2: communication protocol?
Set of rules to communicate(send/receive data) between two devices using wire/wireless(medium/channel)

## Slide 3: Types
Wireless –wifi,bt,zigbee,gsm/gprs
wire
Asynchronous
(no clk)
UART
CAN
Synchronous(clk)
USART
SPI
I2C
Serial(1bit)
Parallel (8bit)
Data transmission methods
Simplex-tx or rx
Half duplex-tx & rx
Full duplex –tx & rx simultaneous

## Slide 4: Serial vs parallel

## Slide 5: Synchronous vs Asynchronous

## Slide 6: Data tramission types

## Slide 7: UART
Universal asynchronous receiver and transmitter
2 wire Serial asynchronous protocol
Full duplex/half duplex
Max distance 15m(rs232)
Baud rate 9600bit/s
Application ->gsm/bt/wifi/rfid

## Slide 8: MCU to MCU/other UART Device interface
Pin details
RC6/TX -output
RC7/RX -input
RC7
RC6

## Slide 9: MCU with PC interface

## Slide 10: UART frame

## Slide 11: Continue…
UART frame congiration
Idle ->clock high
Start bit -> 1 bit clk low
Data bits -> 8bit /9bit
Parity bit ->1 bit even/odd
Stop bit ->1 bit clk high
Baud rate-9600bit/sec
Tx/Rx pin configuration in TRISC

## Slide 12: Baud rate calcuation
Baud rate = FOSC / (64 *(x+1)) if BRGH=0
Baud rate = FOSC / (16 *(x+1)) if BRGH=1
X+1 = FOSC/ 16*Baud rate
X+1 = 4mhz /(16*9600)
X=26-1 =25
SPBRG = x
1 bit time = 1/9600 =104us

## Slide 13: Tx block diagram

## Slide 14: Tx registers

## Slide 15: Rx block diagram

## Slide 16: Rx registers

## Slide 17: UART with PIC

## Slide 18: Tx code
TRISC6=0; //tx output
TRISC7=1; //rx input
TXSTA=0x26; //tx register
RCSTA=0x80; //serail port enable
SPBRG=25; //baud rate generator

## Slide 19: Rx code
TRISC6=0;
TRISC7=1;
TXSTA=0x26;
RCSTA=0x90; //Continuous Receive Enable bit
SPBRG=25;

## Slide 20: Possible Errors
Software errors
Over run error -> if rx reg receive bytes repeat
Under run error ->tx buffer empty ,stop bit append if not append ,not idle high error occur
Framing error ->if rx reg receive bytes repeat or stop bit not occur
Parity error ->parity bits mismatch
Break condition ->if stop bit not occur for long time
Harware errors
Tx,rx,gng connection on both tx and rx devices and supply 5v
Baud rate 9600 std
Distance within 15m
Tx,rx pin output and input config and connection
Delay for each bit transmission should correct

## Slide 21: Tasks
Mcu to mcu
Mcu to gsm/gprs (sim800a/c)
Mcu to rfid (em-18)
Mcu to gps(NEO-6M )
Mcu to Mcu to bluetooth(hc-05)
Mcu to wifi(esp8266)