## Slide 1: ARM –advances RISC machine

## Slide 2: History
Manufactures –ARM
vandors
  STM
  Nxp/freescle
  TI
Applications –mobiles,computer,advances medical devices,robotics
Advantages –low power ,high spee,more features ,debugger,clock controls,high data size,various operating mode,high instruction set,high pricisions,more IDE,community support

## Slide 3: Family
ARM 1 to ARM 7  old core
CORTEX –A (application)
CORTEX –R (real-time)  new core
CORTEX –M (microcontroller)
ARM7 | cortex
ARM(32 bit) and Thumb(16bit) instruction set Switchable | Thum-2 fixed 16 and 32 bit instruction set
Support 7 operating modes | No operating modes
Used in old small application | Used in advance application
3.3 v operating volt | 3.3 v operating volt
Register map registers | No register map,have to use plugins or have to write own drivers from scratch

## Slide 4: STM32F103c8 core specs
32bit controller , RISC, Harvard architecture
32 bit address and data bus
Program memory -64/128kb
Data memory -20kb
Interrupts -256 ->240 usable NVIC
Peripherals- 7 timers,adc,ccp,3 uart,2 spi,2 i2c,can,usb
GPIO pins -48  36 usable
Instruction cycle – 3 pipeline stage
Clock
  Int -8mhz
  Ext-4-20mhz
  PLL-max 72 max

## Slide 5: Pin details

## Slide 6: Bus
Address bus
Data bus
Control bus
System bus
AHB
APB1,APB2

## Slide 7: Core architecture

## Slide 8: PLL- phase lock loop

## Slide 9: PLL waveform

## Slide 10: GPIO Registers
GPIOx_CRL - below pin 8
GPIOx_CRH - above pin 7 & below pin 16
GPIOx_IDR
GPIOx_ODR
Each 32bit registers
Modes in GPIO_CRL
    00- input
    01- output-10mhz
    10-output-2mhz
    11-output-50mhz
Config type GPIO_CRH
input output
      00-anolog 00-GPIO pushpull
      01-input floating 01-GPIO open drain
      10-input push pull 10-alterfunction pushpull
      11-Reserved 11-alterfunction opendrain

## Slide 11: Driver code explanation
Project creation in keil with legacy package install
Stm32 cube clock configuration
Software debug in keil
Hardware debug in keil
Register map
Pll config sys_stm32f1X.c(startup) edit for 60mhz
Gpio.h
Gpio.c
Src.c led blinking ,switch