## Slide 1: timers

## Slide 2: Timer vs delay

## Slide 3: Timer vs cpu clock

## Slide 4: Timer vs counter
Timer | Counter
Internal clock | External clock
Automatic counting to generate delay | Event generate counting from sensors or switches
Timer mode | Watchdog mode

## Slide 5: Types
Timer0-8 bit (internal and external clk)
Timer1-16 bit (internal and external clk)
Timer2-8 bit (internal clk)

## Slide 6: Registers
OPTION
TMR0

## Slide 7: How Works

## Slide 8: TIMER0 CALCULATION
COUNT = FOSC / (4 * PRE * (256 – TMR0 ) * FREQ )
FOSC = 4MHZ -20 MHZ
PRE = 2 TO 256 (TMR0 RATE)
1 TO 128 (WDT MODE)
TMR0 = 0 TO 255
FREQ = 1/T
1 SEC = 1HZ
1MS = 1000HZ

## Slide 9: Program
Timer0_init(void)
Timer0_sec(unsigned int delay)
Timer0_ms(unsigned int delay)

## Slide 10: Timer1
16BIT both timer and counter
More delay can generate than tmr0 and tmr1

## Slide 11: Timer1 registers
T1CON
TMR1L
TMR1H

## Slide 12: HOW WORKS

## Slide 13: TIMER1 CALCULATION
COUNT = FOSC / (4 * PRE * (65536 – TMR1 ) * FREQ )
FOSC = 4MHZ -20 MHZ
PRE = 1 TO 8
TMR1= 0 TO 65536
FREQ = 1/T
1 SEC = 1HZ
1MS = 1000HZ

## Slide 14: Timer2
8BIT only timer
Used in PWM application
Compare to tmr1 and tmr0 accurate time

## Slide 15: Timer2 registers
T2CON
TMR2
PR2

## Slide 16: HOW WORKS

## Slide 17: TIMER2 CALCULATION
COUNT = FOSC / (4 * PRE * (PR2 – TMR2 ) * FREQ )
FOSC = 4MHZ -20 MHZ
PRE = 1 TO 16
TMR0= 0 TO 255
PR2= 0 TO 255
FREQ = 1/T
1 SEC = 1HZ
1MS = 1000HZ

## Slide 18: Tasks
1ms delay
1 sec delay
Dynamic time driver in ms and sec
1 min motor on and off using switch