## Slide 1: Communication protocols
SUMMARY

## Slide 2: COMMUNICATION PROTOCOLS
wire
Asynchronous
(no clk)
UART
CAN
Synchronous(clk)
USART
SPI
I2C
Serial(1bit)
Data transmission methods
Simplex-tx or rx
Half duplex-tx & rx
Full duplex –tx & rx simultaneous

## Slide 3: GENERAL TECH DIFFERENCE

## Slide 4: UART
Universal asynchronous receiver and transmitter
2 wire Serial asynchronous protocol
Full duplex/half duplex
Max distance 15m(rs232)
Baud rate 9600bit/s
Application ->gsm/bt/wifi/rfid

## Slide 5: SPI(serial pheripheral interface)
It is 4 wire serial synchronous protocol(SCL,MISO,MOSI,SS)
Single master multi slave
Max slave depend MCU I/O pins depend
Slave active by SS pin low ,hardware wiring slaves
Hardware address based
Full duplex / Hal duplex data transmission
4 types of communication clock configuration/modes
Max distance 15cm
Max speed 5mhz i.e fosc/4

## Slide 6: I2c (inter integrate circuit)
2 wire serial synchronous protocol(SDA,SCL)
Multi master multi slave connection
Max distance 10cm
Max speed 100khz-or 400khz
Software Address based protocol
127 slaves can connect in 7bit slave address ,1023 slaves can connect in 10 bit slave address
Half duplex data transmission only
2 operating mode
  Master (tx /rx )
  Slave (tx /rx )

## Slide 7: CAN(CONTROL AREA NETWORK
developed by bosch in 1980 for automotive industry
2 wire serial asynchronous protocol(CAN H,CAN L)
Multi master protocol
Max distance 40m if 1MBPS , 250m if 250kbps
Max speed -1mbps
Message based protocol
half duplex data transmission
Sent data in differential signal
Upto 127 nodes can connect on can bus
Can bus has hot-plugging feature (i.e) we can connect node while can bus in working

## Slide 8: continue
high speed, high noise immunity,error detection
Auto retransmission,error confinement
No host and target communication (i.e) no source and destination address
Broadcast type communication
It reduce connection complicity

## Slide 9: CONNECTIONS DIFFERENCES

## Slide 10: connections

## Slide 11: MCU to MCU/other UART Device interface
Pin details
RC6/TX -output
RC7/RX -input
RC7
RC6

## Slide 12: MCU with PC interface

## Slide 13: SPI connection
*Normal spi connection using separate SS pins
*Daisy chain connection by same SS pin

## Slide 14: I2c bus
1k -400khz
2.2k (100-400khz)
4.7k -100khz

## Slide 15: I2c bus circuit

## Slide 16: CAN BUS

## Slide 18: PROTOCOL FRAMAES

## Slide 19: UART frame

## Slide 20: I2c frames format

## Slide 21: I2c frames

## Slide 22: I2c frame

## Slide 23: Can frames
Data frame
Remote frame
Error frame
Overload frame

## Slide 24: DATA FRAME-Standard can & Extended can

## Slide 25: TIMING DIAGRAMS and CLOCKS

## Slide 26: UART frame

## Slide 27: SPI clock modes

## Slide 28: SPI timing or clock diagram

## Slide 29: Continue..

## Slide 30: I2c frame clocks

## Slide 31: Can signalling

## Slide 32: can-bus volt levels or timing diagram

## Slide 33
 | UART | SPI | I2C | CAN
DEVELOPERS | NXP | MOTOROLA | NXP | BOSCH
TX TYPE | ASYN | SYN | SYN | ASYN
WIRE | TX,RX (2) | SCLK,MISO,MOSI,SS (4) | SCL,SDA(2) | CAN H ,CAN L(2)
TX SIGNAL | DIGITAL | DIGITAL | DIGITAL | DIFFERENTIAL
MODE | TX-RX | SINGLE MASTER MULTI SLAVE | MULTI MASTER MULTI SLAVE | MULTI MASTER
TRANSFER TYPE | FULL DUPLEX | FULL DUPLEX | HALF DUPLEX | HALF DUPLEX
DISTANCE | 15M(rs232) | 15CM | 10CM | 40M@1mbps
SPEED/TRANFER RATE | 9600BIT/SEC 115200bit/sec | MAX 10MBPS | 100KHZ/400KHZ | 1MBPS Can fd-2mbps
ARBITRATION | NO | NO | YES | YES
CLOCK STRETCH | - | - | YES | -
ADDRESS TYPE | - | HARDWARE | SOFTWARE | MESSSAGE

## Slide 34
 | UART | SPI | I2C | CAN
RESISTOR TYPE | - | - | 4.7K@100KHZ | 120 OHM
NO.OF.DEVICE | 1 | DEPENDS MCU | 127@7BIT ADDR, 1023@ 10BIT ADDR | UPTO 127 nodes
HOT PLUG | - | - | - | YES
BROADCAST | - | - | YES | YES
APPLICATION | BT,WIFI,GSM AND CORE(cpu) | DISPLAY,SD module AND CORE(cpu) | MULT CORE(dual core,quad core) AND DEVICE(sensors,display) | VEHICLES ECU CONECTION,MULTI CORES(ECUs)