## Slide 1: SPI

## Slide 2: SPI(serial pheripheral interface)
It is 4 wire serial synchronous protocol(SCL,MISO,MOSI,SS)
Single master multi slave
Max slave depend MCU I/O pins depend
Slave active by SS pin low ,hardware wiring slaves
Hardware address based
Full duplex / Hal duplex data transmission
4 types of communication clock configuration/modes
Max distance 15cm
Max speed 5mhz i.e fosc/4

## Slide 3: SPI connection
*Normal spi connection using separate SS pins
*Daisy chain connection by same SS pin

## Slide 4: SPI clock modes

## Slide 5: SPI timing or clock diagram

## Slide 6: Continue..

## Slide 7: How works

## Slide 8: Block diagram

## Slide 9: Registers
SSPCON -control reg
SSPSTAT -status reg
SSPBUF -storage reg

## Slide 10: SSPCON1

## Slide 11: SSPSTAT

## Slide 12: Program for master
Master_init()
Master_write()
Master_read()

## Slide 13: Program for slave
slave_init()
slave_write()
slave_read()

## Slide 14: Tasks
Mcu to mcu
Mcu to mcp4922
Mcu to mcp3008
Mcu to nrf24101